## Slide 1
House Cleaner Robot
Autonomous coverage cleaning — ROS 2 + Nav2 + Gazebo
Architecture, control stack, and the failure modes that were measured and fixed
ACTION
NavigateToPose
/navigate_to_pose
SERVICE
CreepToDock
/creep_to_dock
TOPIC
BatteryState
/battery_state
TOPIC
Bool (latched)
/dock/seated
Every subsystem communicates only through these contracts — which is why mode:=sim and mode:=real run the same supervisor.
Notes: Framing: this is a contract-driven autonomy stack. The mission layer never imports simulator code, which is what makes the sim-to-real swap a launch argument rather than a rewrite.

## Slide 2
Scope & design principles
What this system is, and the constraints it was built under
2/16
1. Hardware-agnostic mission layer
The supervisor talks only to Nav2 actions, ROS topics and two custom services. battery_sim and battery_hw are interchangeable backends behind the same /battery_state + /dock/state contract.
2. Portability by detection
No hardcoded distro, username or path. ros-distro.sh resolves ROS_DISTRO, CONTAINER_NAME and IMAGE_NAME from what is installed; every script sources it.
3. Fail-fast, then skip
A bad coverage cell costs one bounded timeout (45 s) or a detector trip (~15 s — NAV_SILENT). It never blocks the mission.
4. Single safety gate
Both Nav2 output and the docking creep are published to /cmd_vel_nav, so velocity_smoother and collision_monitor gate every command.
Stack: ROS 2 (rclpy) · Gazebo · slam_toolbox · Nav2 (MPPI + NavFn) · ros_gz_bridge · Foxglove · Docker
Notes: The four principles are the review checklist. Any proposed change that breaks one of them (e.g. importing simulator internals into the supervisor) is rejected.

## Slide 3
Node graph & topic contracts
Processes, the interfaces between them, and the direction of data
3/16
Simulation
gz sim (house_room.world) ros_gz_bridge → /scan /odom /tf /clock
Localization
slam_toolbox (async) → /map + map→odom TF
Application nodes
mission_supervisor battery_sim (or battery_hw) docking_controller
Nav2 lifecycle stack (brought up by retry loop, not lifecycle_manager)
bt_navigator
NavigateToPose → behavior tree
planner_server
NavFn Dijkstra → /plan
controller_server
MPPI → /cmd_vel_nav
behavior_server
spin / backup / drive_on_heading
velocity_smoother
/cmd_vel_nav → /cmd_vel_smoothed
collision_monitor
/cmd_vel_smoothed → /cmd_vel
/cmd_vel → ros_gz_bridge → gz DiffDrive plugin
Config is bind-mounted, so src/ and YAML edits need no rebuild — relaunch picks them up (symlink-install).
Notes: Walk the chain left to right. The key point: controller_server is remapped to cmd_vel_nav so its raw output never reaches the robot directly.

## Slide 4
The velocity chain
Four stages, one message type — and the bug that breaks it
4/16
controller / behavior / docking
/cmd_vel_nav
velocity_smoother
/cmd_vel_smoothed
collision_monitor
/cmd_vel
ros_gz_bridge
gz.msgs.Twist
Rates: 20 Hz controller · 20 Hz smoother · 20 Hz monitor · collision_monitor source_timeout 3.0 s
Failure mode: type mismatch
Newer distros default enable_stamped_cmd_vel: true (TwistStamped). velocity_smoother, collision_monitor and the gz bridge all speak plain geometry_msgs/Twist, so the smoother receives nothing and the robot never moves — with no error logged anywhere.
Fix
controller_server:
ros__parameters:
enable_stamped_cmd_vel: false
behavior_server: # same
velocity_smoother: # same
collision_monitor: # same
Rule: every stage in the chain must agree on the message type. Verified with ros2 topic hz on each stage.
Notes: This is the highest-value slide for anyone porting the stack to a new distro. Symptom is 'no motion, no errors'.

## Slide 5
Startup & the lifecycle gate
Why goals are not sent until three nodes report ACTIVE
5/16
1. gz sim + bridge
Gazebo starts, bridge republishes /clock /scan /odom /tf
2. slam_toolbox
configure + activate via retry loop (120×1 s). No Bond server, so no lifecycle_manager.
3. Nav2 nodes
8 nodes, each configure then activate, retried. Ends with the READY marker.
4. Supervisor wait
Concurrent wait on /map AND the NavigateToPose action server, 180 s cap.
5. ACTIVE gate
Polls get_state on bt_navigator, velocity_smoother, collision_monitor; requires id == 3.
6. Plan + first goal
Coverage goals built from the live map; goal 1 gets a 90 s timeout.
Cause of the gate: the NavigateToPose server is advertised before the node is ACTIVE, and velocity_smoother/collision_monitor activate LAST.
Notes: Without step 5 the controller accepts a goal while the velocity chain is dead. That looks like a stall, which fed a watchdog restart loop.

## Slide 6
Coverage planning: boustrophedon
Pure-Python geometry in house_cleaner_core, unit-testable without ROS
6/16
row endpoints become navigation goals
two goals per row, alternating yaw (0 / π)
coverage_bounds(grid, 0.55)
Coverage rectangle from the SLAM map window, inset 0.55 m to clear the 0.30 m inflation band.
build_boustrophedon(bounds, 0.45)
Rows 0.45 m apart; each row contributes its two endpoints, with alternating yaw.
snap_to_free_row(grid, x, y)
Plan-time snap: nearest cell with 0 ≤ occupancy < 50; unknown (-1) is never a goal.
revalidate_goal(...) before every goal
Re-checks the newest costmap, sweeps ±2 m along the row, or drops the goal with a reason.
Static furniture AABBs are excluded twice: at plan time (in_furniture_keepout) and again at goal time.
Notes: geometry.py is deliberately ROS-free so the coverage maths can be unit-tested headlessly. Function names are the real API.

## Slide 7
Planning & control: NavFn + MPPI
Global grid search, then a sampling-based local controller
7/16
planner_server · NavFn
Dijkstra expansion over the global costmap, then backtrack. allow_unknown: true (early SLAM map is mostly unknown). tolerance: 0.30 — must stay ≤ the goal checker's xy tolerance or the goal can never be satisfied.
controller_server · MPPI
Samples noisy velocity rollouts, scores them with weighted critics, and averages the best. batch_size 600 · time_steps 56 × model_dt 0.05 s (2.8 s horizon) · temperature 0.5 · gamma 0.015 · 20 Hz.
MPPI critics and weights
PathAlign 14.0
PathFollow 7.0
Goal 5.0
Constraint 4.0
Cost 3.5
GoalAngle 3.0
PathAngle 2.0
PreferForward 0.0
Consequence of PreferForward = 0.0: reverse is free, which is what lets the robot back out of furniture corners. The trade-off is that the cost gradient can vanish near a goal, so MPPI may stop ~0.28 m short — hence xy_goal_tolerance 0.30 and the NAV_SILENT detector.
Notes: Critic weights are the actual YAML values. The 0.0 on PreferForward is a deliberate choice with a documented trade-off.

## Slide 8
SLAM & costmaps
slam_toolbox scan matching, and the costmap that feeds NavFn
8/16
slam_toolbox (async)
resolution 0.05 m, mode: mapping, scan_period 0.1 s
minimum_travel_distance 0.15 m minimum_travel_heading 0.20 rad
Both must stay BELOW the 0.48 m undock move. At the original 0.5 m the final undock never triggered a scan match, so map→odom stayed stale, the robot's map pose sat inside the dock's lethal cells, and the planner failed with “Failed to create plan” on every goal.
Costmap layers
static_layer
from /map, transient_local subscription
obstacle_layer
/scan, marking + clearing, raycast 3.0 m
inflation_layer
radius 0.30 m, cost_scaling_factor 2.5
robot_radius
0.105 m (Burger)
Critical difference: global_costmap uses track_unknown_space: true, but local_costmap uses false. With true, the rolling window stays ~97% unknown, MPPI treats it as blocked and the robot never moves.
inflation_radius 0.30 m is why coverage goals need a 0.55 m margin — goals must not land inside the inflation band.
Notes: Two parameters caused multi-day bugs: the SLAM travel gate and track_unknown_space on the local costmap.

## Slide 9
Mission state machine
mission_supervisor: the top-level FSM and its guards
9/16
INIT
CLEANING
RETURNING
DOCKING
CHARGING
UNDOCKING
DONE
Transitions
CLEANING → RETURNING
battery ≤ low_threshold (40%) — watchdog timer cancels the in-flight goal
RETURNING → DOCKING
an approach pose reached → /creep_to_dock service
DOCKING → CHARGING
response.seated == true → /dock/command CMD_START
CHARGING → UNDOCKING
percentage ≥ 95% → CMD_STOP → /undock Trigger
UNDOCKING → CLEANING
verified reverse motion ≥ 0.24 m
any → DONE
battery ≤ 1% and not seated (hard abort)
mission.loop := true restarts coverage after the final dock — used for soak testing and demos.
Notes: The FSM is the spine of the supervisor. Each transition has a single observable condition, which is what makes it testable.

## Slide 10
Goal timeouts & the result policy
Every reachable outcome of a NavigateToPose call has a handler
10/16
CLEANING goal 1
90 s
cold start: map/TF still maturing
CLEANING goals 2..n
45 s
normal goal finishes in 4–13 s
RETURNING
90 s
capped by the remaining return budget
mission.return_budget
180 s
wall clock for the whole return phase
progress_checker
0.05 m / 90 s
abort when no progress
charge wait
300 s
bounded; exits early if dock lost
Result handling
SUCCEEDED
advance
ABORTED err=102
TF lag — settle 3 s, retry once
ABORTED other
planner proved it unreachable — skip
TIMEOUT
revalidate, retry once, then skip
NAV_SILENT
MPPI frozen — skip immediately
VEL_STALL
settle, one retry, then skip
RETURN_BUDGET
stop return attempts
BATTERY_EMPTY
abort mission cycle
CANCELED
low-battery cancel → recharge cycle
No status reaches the loop without an explicit handler — that is what keeps a bad cell bounded instead of fatal.
Notes: Statuses are the real string values returned by send_goal(). NAV_SILENT and VEL_STALL are project-specific detectors layered on top of Nav2's statuses.

## Slide 11
Fault detectors & watchdog layers
Three tiers: node timer, mission detectors, host supervisor
11/16
Tier 1 · in-node timer
create_timer(0.5, _watchdog_cb):
• battery ≤ 40% → cancel_goal_async() • battery ≤ 1% → hard cancel • VEL_STALL → cancel • return budget exceeded → cancel
Runs while spin_until_future_complete() renders the node, so it fires even mid-action.
Tier 2 · mission detectors
_nav_abort_reason(), polled at 100 ms:
VEL_STALL
/cmd_vel_nav fresh and v ≥ 0.02, but /cmd_vel silent > stall_hold (8 s) and robot still
NAV_SILENT
controller alive but v,w < 0.02 for ≥ 15 s
Reason strings are returned as the goal status itself.
Tier 3 · host watchdog
watchdog.sh, every 15 s:
• container down • no mission log 180 s • ≥4 stall lines / 100 s with no progress • battery empty, not seated • /cmd_vel_nav ≥ 2 Hz but /cmd_vel < 1 Hz (twice)
Soft: dump + cancel_nav + bounce smoother/monitor. 2 in a row → full stack restart.
Escalation is deliberate: local cancel → bounce the two tail nodes → restart the container.
Notes: Emphasise the debouncing: the chain probe needs two consecutive hits, and any progress marker resets the stuck-pattern counter. Unhysteretic watchdogs caused restart loops.

## Slide 12
Docking: laser-guided creep
Laser sector in the base frame, three independent seat latches
12/16
Front clearance
min range within ±creep.sector_deg (12°) of the forward ray; index from angle_min, not index 0
fwd < 0.13 m
creep.stop_range — geometric seat
stall 2.5 s @ fwd < 0.35 m
odom speed < 0.01 while pressed
6 samples / 3 s, spread < 0.05 m
flat-clearance window latch
Parameters (namespace creep. / undock.)
creep.speed
0.04 m/s
creep.timeout
30.0 s
creep.max_attempts
2
undock.speed
−0.06 m/s
undock.meters
0.48 m
velocity_topic
/cmd_vel_nav
Interface
house_cleaner_msgs/CreepToDock
---
bool seated
float32 front_clearance_m
std_srvs/Trigger -> /undock
Reporting: /dock/seated (std_msgs/Bool) is published TRANSIENT_LOCAL so a late or restarted subscriber still learns the state.
Verification: undock integrates |v|·dt and requires ≥ 0.24 m. If it did not move, seated stays true — the backend can never claim to be charging in free space.
The creep is published to /cmd_vel_nav on purpose: the collision monitor stays the last-resort bumper during docking.
Notes: Three independent latches means a single sensor lie cannot fake a seat. The service interface is the real .srv content.

## Slide 13
Safety chain & collision monitor
Why the stop polygon was removed and what replaced it
13/16
Kept: PolygonSlow
PolygonSlow:
type: polygon
action_type: limit
points: '[0.35,0.15],[0.35,-0.15],
[0.12,-0.15],[0.12,0.15]'
speed_limit_pct: 45.0
Limits speed to 45% inside a 0.12–0.35 m front quad. source_timeout: 3.0 s.
Removed: PolygonStop
action_type: stop deadlocked the chain. While any scan point sits in the polygon the monitor forces output to zero, and after stop_pub_timeout it stops publishing entirely. Because the robot is stopped, the obstacle never leaves the polygon — so /cmd_vel stays silent forever and every later goal looks like VEL_STALL until the stack is restarted.
Smoother configuration (velocity_smoother)
feedback
OPEN_LOOP
max_velocity
[0.65, 0.0, 2.5]
max_accel
[1.5, 0.0, 3.0]
max_decel
[−2.0, 0.0, −3.5]
max_jerk
[3.0, 0.0, 5.0]
cmd_vel_timeout
0.5 s
Lesson: a fail-safe that stops publishing is not fail-safe for the rest of the pipeline.
Notes: This is a genuinely counter-intuitive result: the safety feature caused the deadlock. Worth dwelling on for a technical audience.

## Slide 14
Battery model & energy policy
A rate model with hot-tunable parameters
14/16
Model (battery_sim, 0.2 s tick)
if seated and charging and pct < 100:
pct += charge_rate * dt
elif not docked and speed > 0.03:
pct -= drain_rate * dt
# speed from /odom (ground truth),
# /cmd_vel + /cmd_vel_smoothed as backups
Publishing
/battery_state sensor_msgs/BatteryState
percentage is a 0–1 fraction (ROS standard). Publishing 0–100 made a real 0.96% read as 96%, which exited the charge loop immediately.
voltage interpolated 10.0 → 12.6 V linearly with percentage.
Thresholds
low_threshold
40 %
enter RETURNING
charge_target
95 %
resume CLEANING
critical
1 %
hard mission abort
drain_rate
0.20 %/s
hot-tunable
charge_rate
0.80 %/s
hot-tunable
speed_threshold
0.03 m/s
motion gate
$ ros2 param set /battery drain_rate 4.0 # accelerate a demo; 0.20 to restore
Notes: Both rates are re-read every tick, so a live mission can be sped up without relaunch. The 0–1 percentage convention is a classic integration bug.

## Slide 15
Operations: one command, eight checks
Reproducible bring-up, deterministic teardown
15/16
$ ./run_all.sh # kill stale → launch → verify
$ ./run_all.sh --stop # kill only
$ ./run_all.sh --verify # checks only
1
container house_cleaner_<distro> is running
2
gz-sim-main present (docker top)
3
rviz2 present (docker top)
4
log contains 'Nav2 lifecycle bringup complete'
5
Foxglove WebSocket upgrade returns HTTP 101
6
/battery_state publishes (ros2 topic echo --once)
7
watchdog.sh running (pgrep)
8
monitor_loop.sh running (pgrep)
Deployment facts
Base image
ros:<distro>-ros-base
Network
host — DDS discovery is multicast
Workspace
src/ bind-mounted to /workspace/src
GPU order
nvidia runtime → /dev/dri → llvmpipe
Display
X11 preferred (RViz/Gazebo need GLX)
Anti-flicker
vblank_mode=xpresent
Log rotation
json-file, 50 MB × 5
Ports
8765 (Foxglove WebSocket)
Kill order matters: watchdog and monitor die BEFORE docker rm -f, or the watchdog relaunches the container being removed.
Notes: The kill order is a real bug that was fixed: removing the container while the watchdog was alive triggered an unwanted relaunch.

## Slide 16
Engineering takeaways
1
Contracts over coupling
Four interfaces (one action, one service, two topics) let the same supervisor drive a simulator or hardware.
2
Every wait needs a bound and a verdict
Timeouts, detectors and a total-return budget turned unbounded stalls into 15–45 s skips.
3
Measure, then tune
Tolerances, SLAM travel gates and watchdog hysteresis were all set from observed failures — not defaults.
Full detail:
DOCUMENTATION.md
·
CONTEXT.md
(decision ledger)
Code:
src/house_cleaner_mission/mission_supervisor.py
(1193 lines)
Questions welcome — happy to walk the code or run the stack live.
Notes: Close on the three engineering principles, then point at DOCUMENTATION.md for depth.