## Slide 1
House Cleaner Robot
A small robot that cleans a room all by itself
What it does, how it thinks, and how it never gets stuck
Build a map of the room
Clean every part in strips
Battery gets low — it knows
Parks & charges at its dock
Goes back to work again
In one line: it maps the room, cleans it in neat strips, and recharges itself when tired — no human needed.
Notes: Opening line: this is a robot that vacuums a room on its own. Five simple steps. Everything else in this deck explains those five steps.

## Slide 2
What is this project?
The plain-English version
2/16
A robot vacuum that works in a computer, so we can test it safely before buying hardware.
1. Real robot, virtual room
It is a TurtleBot3 Burger robot driving inside a pretend house made in a physics simulator.
2. No map, no problem
It starts knowing nothing about the room and builds the map as it drives around.
3. It charges itself
When the battery runs low it drives back to its dock, charges up, and gets back to work.
4. Built to never get stuck
Three layers of 'babysitters' watch it and fix problems automatically.
You can watch all of it live: the 3D room window, a dashboard view, and a web page in your browser.
Notes: Emphasise the 'why': simulation lets us try dangerous things — running the battery to zero, blocking the dock — without breaking a real robot.

## Slide 3
The robot's day, in 5 steps
The whole mission is one simple loop
3/16
1
Map
learn the room
2
Clean
neat strips
3
Tired
battery low
4
Charge
at the dock
5
Resume
and repeat
…then step 5 loops straight back to step 2, so it cleans pass after pass.
How it decides
It checks its battery level constantly. Below 40% it stops cleaning and heads home.
How it gets home
It remembers where the dock is and drives to a spot just in front of it.
What 'done' means
Battery back to 95% → it reverses out and carries on exactly where it left off.
Notes: This is the single most important slide. If the audience remembers one picture, it should be this loop.

## Slide 4
Step 1 — It learns the room by driving
Like feeling your way around a dark room with a torch
4/16
sofa
table
crates
charging dock
robot's laser
1. Spinning laser
The robot has a laser that measures distance to everything around it, 360 degrees.
2. Map grows as it drives
Every new reading is stitched onto the map. Unknown areas fill in over time.
3. It knows where it is
By comparing readings to the map it always knows its own position.
Notes: Analogy: walking through your own living room in the dark with a flashlight. The map is the picture you build in your head.

## Slide 5
Step 2 — It plans a 'lawnmower' route
The trick that guarantees no spot is missed
5/16
one goal at the end of each strip
green dots = the 'go there' points the robot is given
1. Cover in strips
Parallel rows 45 cm apart. The robot fills each strip, like mowing a lawn.
2. Alternate direction
It turns around at the end of every second strip — no wasted 180° spins.
3. Check before going
Just before driving to a point, it re-checks the latest map. Blocked? It slides 2 m sideways.
4. Skip the furniture
Known furniture is simply banned as a destination — the robot never aims at the sofa.
Notes: Emphasise 'lawnmower' — everyone understands mowing a lawn. 45 cm strips fit the robot's cleaning width.

## Slide 6
Step 2b — How it actually drives there
Two brains: one for the big picture, one for the steering wheel
6/16
Brain 1 — the navigator
Works out the shortest sensible path from here to the next green dot, going around walls and furniture. Re-plans if something new appears.
Brain 2 — the driver
At 20 times a second it imagines 600 possible ways to move in the next 3 seconds, picks the safest one, and applies the wheel and pedals gently.
Every command then passes through the same safety gate:
Navigator picks path
Driver steers
Smoothing (no jerks)
Safety gate (slow near walls)
Robot moves
If any single link in that chain goes quiet, the robot notices within seconds and fixes it instead of sitting there.
Notes: Avoid jargon: 'navigator' vs 'driver' is the clearest way to explain global planner vs local controller.

## Slide 7
Step 3 — It notices it is tired
A simulated fuel gauge the robot checks constantly
7/16
100% → 40% keep cleaning
40%
go home → 1% = emergency stop
It drains for real
The battery empties a little every second the robot is driving — faster if you speed the demo up.
It is checked 2× per second
A dedicated little program publishes the battery level on a topic everyone can read.
40% = time to go home
Crossing 40% cancels whatever chore it is doing and sends it to the dock.
1% = stop everything
Below 1% it refuses to start new work, so it can never die in the middle of the room.
For demos you can speed the battery up, so a whole clean-and-charge cycle takes minutes instead of hours.
Notes: The battery bar is a good place to pause: 40% trigger, 95% resume, 1% hard stop. These three numbers explain the whole energy strategy.

## Slide 8
Step 4 — It parks and charges itself
The hardest centimetres: the last 15 cm into the dock
8/16
1
Drive home
Follows the map to a spot about a metre in front of the dock.
2
Line up
Turns to face the dock squarely.
3
Creep in slowly
Slows to 4 cm per second using only its front laser as eyes.
4
Touch & confirm
When the wall of the dock is 13 cm away it considers itself parked.
5
Charge
Tells the dock to start charging, then waits quietly for 95%.
6
Reverse out
Backs up 48 cm, proves it really moved, and resumes cleaning.
Why it is tricky: the map is a little fuzzy, so it might stop 28 cm short of the dock. The robot therefore uses the laser for the final approach, and tries up to five slightly different parking spots before giving up.
It never pretends to be docked: if it did not move when asked, it says so and the battery will not claim to be charging.
Notes: The dock is where most robotics demos fail. This slide shows the sequence and the safety principle: verify, never assume.

## Slide 9
Step 5 — Why it never gets stuck
Three layers of babysitters, from inside the robot to the host PC
9/16
1
Layer 1 — inside the robot
A watchdog timer checks the battery twice a second and cancels the current chore the moment it gets low.
2
Layer 2 — the robot's instinct
It measures its own movement. If it is told to drive but nothing happens for 15 seconds, it gives up on that spot and moves on.
3
Layer 3 — the computer watching
A separate program on the host reads the logs. If the robot is silent, stuck or repeating the same failure, it restarts the affected parts — and the whole simulation if needed.
Result: the robot skips one bad spot and carries on. It does not freeze, and it does not restart the whole simulation.
Notes: The key insight: recovery is layered. Small problems are fixed locally in seconds; only a real crash escalates to a full restart.

## Slide 10
What the robot is made of
Four groups of programs, each with one plain job
10/16
Eyes & ears
Laser, wheel sensors, camera-less mapping. 'What is around me?'
Gazebo simulator
Laser scan
Live map (SLAM)
The driver
Path planning, steering, obstacle avoidance, smooth accelerations.
Navigator
Driver (MPPI)
Safety gate
The brain
The to-do list: clean → park → charge → resume, plus all the checks.
Mission supervisor
Battery model
Docking controller
Watching it
Windows and web pages so a human can see what is going on.
3D room window
Dashboard
Log files
Everything talks over 'ROS 2' — think of it as a postal service inside the robot that delivers messages between programs.
Notes: Analogy for ROS 2: a postal service. Each program posts messages to a mailbox and others subscribe to it. No program is wired directly to another.

## Slide 11
Nice numbers to remember
The tuning that makes it work in practice
11/16
45 cm
Cleaning strip width — how far apart the mowing lines are
40 %
Battery level that sends the robot home
95 %
Battery level at which it goes back to work
13 cm
Distance to the dock that counts as 'parked'
30 cm
How close counts as 'arrived' — because maps are fuzzy
15 s
Silence that means 'stuck here', then it skips that spot
3
Babysitter layers watching for trouble
Notes: These are the numbers an audience usually asks about. Each one came from a real failure that was measured and fixed.

## Slide 12
How to run it (one command)
No expertise needed — the script cleans up and checks itself
12/16
./run_all.sh
1. Cleans up
Closes anything left over from a previous run, so you never get two robots fighting.
2. Starts everything
The room, the robot, the dashboard, the web view, the battery model and the babysitters.
3. Checks itself
Runs eight health checks and prints a tidy list. Look for eight green OK lines.
Stop it with: ./run_all.sh --stop Check it again with: ./run_all.sh --verify
Notes: Stress that the user types exactly one command. The script handles permissions, stale containers and verification on its own.

## Slide 13
What you actually see
Three windows, one story
13/16
The 3D room
The robot driving around the furniture in a physical simulation. Watch it sweep the room in strips.
Gazebo window
The robot's dashboard
Live map, laser dots, planned route, robot position. The engineer's view.
RViz window
The web view
The same information in a browser tab, useful for showing other people on their own screen.
app.foxglove.dev + ws://localhost:8765
The logs
Text files quietly recording every decision: what it cleaned, when it charged, what went wrong.
/tmp/opencode/*.log
A full cycle — clean, park, charge, resume — takes a few minutes when the battery is sped up for a demo.
Notes: If demoing live, open the 3D window first and let it run while talking.

## Slide 14
The tricky parts (and how they were solved)
Honest list — these are the things that actually broke
14/16
The robot would not move at all
Two programs disagreed about the message format for the wheels.
Make every program speak the same plain format.
It aimed at the sofa
The map sometimes says furniture is 'unknown', not 'blocked'.
Ban known furniture as a destination, and re-check each spot before driving.
It froze next to the table
The steering algorithm can give up near a goal, silently outputting zero.
Detect 15 s of silence, skip that spot, move on.
It got 'stuck' forever at the dock
A safety rule stopped the robot and then stopped talking to it.
Replace the hard stop with a slow-down rule.
After docking, the map was wrong
The mapping update needs movement; the undock move was slightly too short.
Lower the movement needed to update the map.
symptom
real cause
fix
Notes: This slide builds credibility: the system works because each of these was found and fixed by measuring, not guessing.

## Slide 15
What is next
Clear, honest roadmap
15/16
Clean better
Dwell longer on dirty spots and re-plan as the map fills in.
Handle several rooms
Split a home into rooms and clean them one by one.
Smarter docking
Use a visual marker for millimetre-accurate parking.
Smoother odometry
Combine wheel and sensor data so the map drifts less.
Automatic testing
Run the whole simulation automatically on every change, so nothing breaks quietly.
Run on real hardware
The same software already supports a real TurtleBot3 — finish validating it.
None of this changes the core idea: map it, clean it, charge itself, repeat.
Notes: Keep it short. The roadmap signals the project is alive without overselling.

## Slide 16
Three things to remember
1
It figures out the room itself
No map is given to it. It drives, looks, and builds its own plan.
2
It takes care of itself
Watches its battery, parks, charges, and gets back to work without help.
3
It cannot get permanently stuck
Three layers of watchdogs notice problems and fix them automatically.
Questions welcome — and you can watch the whole thing run live.
Notes: Close with the three-line summary, then offer the live demo.